## Slide 1
KPED Kitt Peak EMCCD Demonstrator
Instrument
Science
Hardware
ZTF transient follow-up (GWs, SGRBs, TNOs)
Ahumada/Coughlin/Dekany/Kulkarni
Instrument: Coughlin, Dekany, Feeney, Kulkarni, Riddle
Science: Ahumada, Burdge, Coughlin, Dekany, Fuller, Kulkarni, Prince, Riddle
1. EMCCD – Andor iXon 888
2. Filter Wheel – Finger Lakes (10 slot)
3. Filters – Johnson UBVRI, Sloan g and r
4. Corrector Lens
5. Mounting plates
6. Computer
Software
1. EMCCD – Andor SDK + Python wrapper
2. Filter Wheel – FLI SDK + Python wrapper
3. Telescope Control – Robo-AO
4. Reductions – Robo-AO + Chimera
WD Binaries – PTF and ZTF
Burdge/Coughlin/Prince/van Roestel
Gravitational Lens Time Delays
Coughlin
Feeney/Riddle/Dekany/Coughlin
Riddle/Duev/Coughlin
Astroseismology
Fuller
Calibration/Technical
Coughlin
A sensitive, flexible, multi-spectral optical imaging capability for high-cadence follow-up of the transient universe.
Telescope/Camera
Feeney/Riddle/Dekany/Coughlin
1. F/# = 4.864
2. FOV = 4.4 x 4.4 arcmin
3. 2.1 meter primary

## Slide 2
KPED Kitt Peak EMCCD Demonstrator
Science
Asteroseismology
WD Binaries - PTF, ZTF and ATLAS
ZTF transient follow-up (GWs, SGRBs)
Gravitational Lens Time Delays
Calibration/Technical
Photometric stability and performance of EMCCDs as a function of EM gain.
Multiband colors in UBVRI of hot DA white dwarf stars from Gaia.
Monitoring of the ZTF transients identified in the SGRB follow-up work.
ZTF transients, especially those identified as fast fading, in preparation for SGRB and GW follow-up, is important.
Time delay measurement for GAIA + PS1 lens systems
https://arxiv.org/abs/1803.07601
Monitoring of the WD binary systems identified in the original PTF data.
Follow-up of potential ZTF WD binary systems
Follow-up of potential ATLAS WD binary systems
Low-mass pulsating white dwarfs

## Slide 3
KPED Kitt Peak EMCCD Demonstrator
Objects
Papers
Known Objects
ZTF transient follow-up – GRB180523
Coughlin/Ahumada
1. ZTF18aalrxas – 1a?
2. 1821i - ZZ Ceti pulsator with a 4.8 minute period
3. PG-1336 - Eclipsing binary with an orbital period of ~2.4h and also shows pulsations.
PTF/ZTF Periodic Objects
We have confirmed many periodic objects at this point.
ATLAS18qqn early photometry/spectra
Perley/Coughlin/Ahumada
1815f – 7 minute eclipsing binary
Burdge/Prince/Coughlin/Kulkarni
Riddle/Duev/Coughlin
AMCvn SDSS J141118.31+481257.6
Kupfer/Burdge/Prince/Coughlin
Instrument/Technical
Coughlin/Ahumada/Burdge/Feeney
External Objects
ATLAS18qqn – About a week of photometry in UgrI
D6-2 – Hypervelocity white dwarf from Gaia, a few nights of a few hours each
Maxi-J1820+070 – 17 hour period, 0.4 mag
PTF Periodic Objects
Burdge/Prince
ZTF Periodic Objects
Coughlin/Burdge/Prince

## Slide 4
KPED Kitt Peak EMCCD Demonstrator
ZTF Transients (ZTF18aalrxas)

## Slide 5
KPED Kitt Peak EMCCD Demonstrator
AT2018cow

## Slide 6
KPED Kitt Peak EMCCD Demonstrator
ZTF ToO Follow-up

## Slide 7
KPED Kitt Peak EMCCD Demonstrator
Needle in a haystack